## Slide 1: BlackSmith: Scalable RowHammering in the Frequency Domain
William J. Hutton, III, PhD, CISSP Washington State University—CptS 260
December 2, 2021
Notes: Source and inspiration for this presentation: Steve Gibson’s “Security Now” podcast episode 845 (https://www.grc.com/securitynow.htm)

## Slide 2: Overview
What is BlackSmith? (and what is RowHammer?!)
Bit Flipping for fun and profit
Coverage
Mitigation

## Slide 3: What is BlackSmith?
(and a brief introduction of RowHammer)

## Slide 4: BlackSmith: Scalable RowHammering in the Frequency Domain
Security research conducted by COMSEC (Computer Security) group of ETH Zurich (Switzerland)
BlackSmith will be presented at the 43rd Security & Privacy symposium on May 22-26, 2022
IEEE’s “Security & Privacy” is a preeminent cyber security publication and conference.
Notes: Consider joining IEEE (or ACM) as a professional organization.

## Slide 5: BlackSmith: Scalable RowHammering in the Frequency Domain
BlackSmith will be presented at the 43rd Security & Privacy symposium on May 22-26, 2022
IEEE’s “Security & Privacy” is a preeminent cyber security publication and conference.
COMSEC looks at the attack surface of the “whole stack” when it comes to security.
Notes: Consider joining IEEE (or ACM) as a professional organization.

## Slide 6: BlackSmith: Scalable RowHammering in the Frequency Domain
IEEE’s “Security & Privacy” is a preeminent cyber security publication and conference.
COMSEC looks at the attack surface of the “whole stack” when it comes to security.
  (Hardware, software, OS, applications, network, protocols, data, people)
Notes: Consider joining IEEE (or ACM) as a professional organization.

## Slide 7: BlackSmith is the maturation of the 2015 RowHammer attack
RowHammer
  Initial research (October 2014) did not indicate a security problem
  CVE-2015-0565 (January 2015) begins to weaponize this research
RowHammer: is a security exploit that takes advantage of an unintended and undesirable side effect in DRAM in which memory cells interact electrically between themselves by leaking their charges, possibly changing the contents of nearby memory rows that were not addressed in the original memory access1.
Violates isolation
High cell density in modern DRAM
Triggered by specially crafted memory access patterns
Notes: 1. https://en.wikipedia.org/wiki/Row_hammer#Overview

## Slide 8: RowHammer details
Side effect is triggered by patterns that rapidly activate the same cells multiple times
Core memory[2,3] (1955-1975) was also sensitive to memory access patterns.
”Checkerboard” diagnostics were run before computation to reveal any problems.
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0
Notes: 2: https://en.wikipedia.org/wiki/Magnetic-core_memory
3: “Turing’s Cathedral” is an excellent book if you’re interested in early computing hardware

## Slide 9: RowHammer details
Side effect is triggered by patterns that rapidly activate the same cells multiple times
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 10: RowHammer details
Side effect is triggered by patterns that rapidly activate the same cells multiple times
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 11: RowHammer details
Side effect is triggered by patterns that rapidly activate the same cells multiple times
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 12: RowHammer details
Side effect is triggered by patterns that rapidly activate the same cells multiple times
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 13: RowHammer details
Side effect is triggered by patterns that rapidly activate the same cells multiple times
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 14: RowHammer details
Side effect is triggered by patterns that rapidly activate the same cells multiple times
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 15: RowHammer details
Side effect is triggered by patterns that rapidly activate the same cells multiple times
In this case the charge leaks to the yellow cell, but the impacted cell already has the same charge, so the bit IS NOT flipped.
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 16: RowHammer details
Side effect is triggered by patterns that rapidly activate the same cells multiple times
However, if the charge leaked to the red cell, the bit would be flipped.
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 17: RowHammer details
The next problem is if this flipped bit is of any significance.
This example is called a “1-sided aggressor row” and is a “term of art” when it comes to RowHammer attacks.
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 18: RowHammer details
Other patterns include:
  “2-sided” aggressor row attacks
  “n-sided” aggressor row attacks
But all RowHammer attacks use uniform patterns.
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0
Notes: In this case, the red cell bit would be flipped, as the cell below it contains a 1.
The next problem is if this bit is of any significance.

## Slide 19: RowHammer Mitigations
RowHammer is not a vulnerability that can be fixed in existing devices (similar to Spectre and Meltdown attacks).
These are design choices. New secure designs are required. Old devices must be replaced.
New DRAM (DDR4) has anti-RowHammer mitigations like TRR (Target Row Refreshing).
But cyber attacks and defense (mitigations) are co-evolutionary! As defenders “catch up” to new attackers, the attackers’ new attacks get better.

## Slide 20: Evolution of RowHammer
“Attacks only get better.” -- Bruce Schneier
RowHammer attacks are practical!
Work in the real word (web browsers, smart phones, in the Cloud, and across the Internet):
SMASH Attack (JavaScript web page bit flipping)
DRAMMER (Deterministic bit flipping on mobile devices)
Flip Feng Shui (Software “needle in a haystack” bit flip)
Throw Hammer (Remote bit flipping via network)

## Slide 21: And now… BlackSmith CVE 2021-42114
BlackSmith: resulted from research into new, non-uniform access patterns that are frequency based and bypass TRR on standard PCs using “fuzzing”.
Unfortunately, BlackSmith demonstrates RowHammer bit flipping on ALL DDR4 devices tested with little effort.
  Search space of non-uniform access patterns is MASSIVE!
  Basic research question, “Which access patterns still flip bits?”
    Fuzzing varies the order, regularity, and intensity of ”aggressor rows”
    Observations matched well-known input parameters in the frequency domain (frequency, amplitude, and phase)
    N-sided patterns still trigger bit flips 31% of the time!

## Slide 22: Some quick examples
Notes: https://www.quora.com/What-is-the-difference-between-phase-modulation-and-frequency-modulation
In phase modulation, the amplitude and frequency remain constant, but the phase reference (angle) changes signaling a 1 to 0 or 0 to 1, depending on what is carried on the line. (DC electricity is transmitted in three phases—that’s why you see three wires on power poles.). Disclaimer: I’m not a EE! 

## Slide 23: What is a fuzzer?
Fuzzers are a security tool that (randomly) varies input and notes output.
BlackSmith fuzzes access patterns on DRAM device over a period of 12 hours.
Learns best access pattern over 256 MB
Processor access to DRAM bypasses L1, L2, and L3 cache and is SLOW
Reported a large number of bit flips in 2:3 vendors (anonymized results)
f(x) | y
1 | 0

## Slide 24: What is a fuzzer?
Fuzzers are a security tool that (randomly) varies input and notes output.
BlackSmith fuzzes access patterns on DRAM device over a period of 12 hours.
Learns best access pattern over 256 MB
Processor access to DRAM bypasses L1, L2, and L3 cache and is SLOW
Reported a large number of bit flips in 2:3 vendors (anonymized results)
f(x) | y
1 | 0
2 | 3

## Slide 25: What is a fuzzer?
Fuzzers are a security tool that (randomly) varies input and notes output.
BlackSmith fuzzes access patterns on DRAM device over a period of 12 hours.
Learns best access pattern over 256 MB
Processor access to DRAM bypasses L1, L2, and L3 cache and is SLOW
Reported a large number of bit flips in 2:3 vendors (anonymized results)
f(x) | y
1 | 0
2 | 3
3 | 8

## Slide 26: What is a fuzzer?
Fuzzers are a security tool that (randomly) varies input and notes output.
BlackSmith fuzzes access patterns on DRAM device over a period of 12 hours.
Learns best access pattern over 256 MB
Processor access to DRAM bypasses L1, L2, and L3 cache and is SLOW
Reported a large number of bit flips in 2:3 vendors (anonymized results)
f(x) | y
1 | 0
2 | 3
3 | 8
4 | 15

## Slide 27: What is a fuzzer?
Fuzzers are a security tool that (randomly) varies input and notes output.
BlackSmith fuzzes access patterns on DRAM device over a period of 12 hours.
Learns best access pattern over 256 MB
Processor access to DRAM bypasses L1, L2, and L3 cache and is SLOW
Reported a large number of bit flips in 2:3 vendors (anonymized results)
f(x) | y
1 | 0
2 | 3
3 | 8
4 | 15
f = x2 - 1

## Slide 28: What is a fuzzer?
Fuzzers are a security tool that (randomly) varies input and notes output.
BlackSmith fuzzes access patterns on DRAM device over a period of 12 hours.
Learns best access pattern over 256 MB
Processor access to DRAM bypasses L1, L2, and L3 cache and is SLOW
Reported a large number of bit flips in 2:3 vendors (anonymized results)
f(x) | y
1 | 0
2 | 3
3 | 8
4 | 15
f = x2 - 1
Now, what could go wrong when we fuzz input?
Are we able to transition from a secure state to an insecure state?

## Slide 29: Bit Flipping for Fun and Profit

## Slide 30: ”What could possibly go wrong?”
Bits are the fundamental unit of digital information.
The binary digits are 0 and 1, on/off, yes/no, true/false
Change page table ids and pivot to attacker control
Change control bits; e.g., ReadOnly to ReadWrite, Execute bits, etc.
Also consider side-channel attacks on secure systems like RSA keys, sudo authentication mechanisms, flow control, etc.

## Slide 31: Coverage
How widespread is the vulnerability?

## Slide 32: BlackSmith tested against three vendors
Think about experiment design: How many vendors should you evaluate?
  Just three vendors (Samsung, Micron, and SK Hynix) cover 94% of the RAM market.
  40 different devices in test pool
  BlackSmith was effective on 100% of the devices in the test pool!

## Slide 33: Mitigation
Can we ever design a truly secure computer system?

## Slide 34: Mitigations
Some DIMMs are more vulnerable than others, but none are safe.
Devices (RAM) in the wild are vulnerable until replaced. (There is no DDR5, yet…)
BlackSmith code is available on GitHub
There is a project with Google to implement BlackSmith in a FPGA
  Hardware test device!
  Find that good vendor
  Test all your RAM and use the least vulnerable
By manufacturer, some had 4 bits flipped, others had 4,000,000 bits flipped!
EEC capable RAM doesn’t prevent RowHammer, but makes it harder.
Notes: EEC requires a pair of bits to be flipped.

## Slide 35: Discussion
Security is porous.
We’ve never seen such pressure on security.
This is a serious problem!
Is it possible to build a secure system? (Why or why not?)